Govno Core 16
  This manual will give you all of the information on how to write programs for a Govno Core 16 16-bit processor.

Contents
  1. Basics
    1.1. About Govno Core 16 and CGovnOS
    1.2. Register layout
    1.3. Memory layout
      1.3.1. Default memory registers
    1.4. Memory addressing types
    1.5. Halt and reboot
  2.
  3. Instruction set lookup table
  4. Footnotes

1. Basics
  1.1. About Govno Core 16
    Govno Core 16 is a 16-bit single-thread processor, that can be emulated using the CGovnOS emulator.
  1.2. Register layout
    Govno Core 16 has only 3 registers. SP, CS and PC. SP is a stack pointer, so it points to the highest stack value[1]. CS is unused by the instructions, so you can use it as a Base Pointer for function scopes (like BP in Intel Processors). PC is a program counter, it points to the instruction currently executing.
  1.3. Memory layout
    Memory layout is really simple. Other processors/RAMs have sections/segments of code, such as .text, .data and .bss. Govno Core 16 doesn’t have these, only one section containing the whole RAM.
    1.3.1. Default memory registers
      SP and CS are set to %FFFF by default, and PC is set to %0000 when reset.

3. Instruction set lookup table
   00 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E 0F
00 NOP CPUID CSP JMP JMI
10 CMP CMIM AND OR XOR NAND NOR NOT PUSH POP DUP SWAP ADD SUB MUL
20 RDD REAB REAW INT DIV
30 LODB LODW
40 CALL RET LSP LCS SSP SCS SPC
50
60
70
80
90
A0 $SPC
B0
C0
D0
E0
F0

%0AA – $SPC – Special VM codes
  %0AA %55 – Halt
  %0AA %56 – Reboot

4. Footnotes
  [1] – (Highest stack value - 1). So if the highest stack value is at %0FFF0, SP would point to %0FFEF.